## Slide 1
Work of others and Customer Research
Image/ Example | Designer | Design Movement | Key info
 | William Morris | Arts and Crafts | British designer in 1880s Simple natural crafts Useful and beautiful products (wallpapers, cushions, etc)
 | Charles Rennie Mackintosh | Art Nouveau | Scottish designer in 1860s – 1920s Known for light and shadow Created stained glass and furniture Inspired by nature and geometric lines
 | Ettore Stottas | Memphis | Italian designer in the 1950s/60s Enjoyed making everyday objects wacky and bold Used lots of bold colours and black lines
Image/ Example | Brand | Key info
 | Alessi | Italian Design Company Homeware and kitchen utensils “Post-modern” style Phillipe Starke is a major designer
 | Apple | USA-based tech company Famous for iconic designs of iPod and iPhone Steve Jobs and Johnathon Ive are major designers Known for innovative and modern design
 | Dyson | British engineering company Famous for vacuum cleaners and innovative technology James Dyson is a major designer
Research
Work or Others
What methods of research can be used to find information?
Case studies
Questionnaires and surveys
Product Analysis
Materials testing
Social media and email
Interviews
Research can be divided into 2 categories; Primary Research and Secondary Research.
Primary is research you complete yourself.
Secondary is research from resources others can gathered e.g. books, magazines and internet
Primary research is generally more reliable as it is done by the person using it and can double-check the data
Another key piece of research, is Anthropometrics and Ergonomics. This helps develop the sizes of products, etc to make sure it fits the User | 
Anthropometrics | The study of measurements of the human body. E.g. Knowing the grip width of a palm, if designing a new travel coffee cup
Ergonomics | The application of anthropometrics to ensure products are safe and comfortable to use. This can also include; size, material, appearance, brightness, sound and texture. E.g. making sure the travel cup is the correct size, and an insulating smooth material to make it comfortable to hold for long periods

## Slide 2
Briefs, Specifications, ideas and development
Design Briefs
A Design Brief is the statement of how you will solve the Design Problem It will often include:
Constraints/ limitations
What the product is
Materials/processes
Any key information you know
Design Specifications
A Design Specification is a list of requirements your product has to meet in order to be successful
It is also useful for evaluation. If your product hasn’t met the Spec then it gives you a starting point for improvements.
Aesthetics | What the product looks like? Style? Colour Scheme? Design Movement?
Customer | Who would buy it? (Age, gender, socio-economic, personality) How does the design appeal to them?
Cost | How much will it cost? (min-max) Why?
Environment | Where will it be used? Why? How will you make it suitable?
Safety | How is it safe? How will it be checked? Why must it be safe?
Size | What is the maximum or minimum size? Why?
Function | What does the product do? What features make it do that function well? How is it unique from similar products?
Materials | What is it made from? Why?
Manufacture | How might it be made? Why? What scale of production? Why?
Technique | Description/ notes | Diagram
Orthographic Projection/ Working Drawings | Includes “Front”, “Plan” and “End” 2D Views, and often an Isometric 3D View Standardised method for scale, dimensions and line types Great for manufacturing | 
Isometric | Common 3D sketching method Can be drawn free-hand or using isometric paper and ruler Angles are at 30 degrees Great for seeing most of the products | 
1-Point Perspective | A 3D drawing method Often used by interior designers and architects Gives drawings depth Only uses 1 vanishing point | 
2-Point Perspective | Used for 3D designs Exaggerates the 3D effect Objects can be drawn above of below the horizon line but must go to the 2 vanishing points | 
Annotated Drawings/ Free and Sketches | Quick and easy way of getting ideas down Range of ideas can be seen Annotation helps explain designs further | 
Exploded View | Helps see a final design of a product and all it’s parts Can see where all the parts fit Great for manufacturers | 
Modelling and Development
Modelling and development are key to testing and improving products
This can be done physically using materials like; card, foam, clay, man-made boards or virtually in CAD
Modelling helps the designer get feedback from the customer, check aesthetics, function, sizes and even materials and production methods and change them if needed

## Slide 3
Design Strategies
Design Strategies are used to solve Design Fixation, and help develop creative design ideas.
Iterative Design
A Proposal is made
It is then planned and developed to meet the brief
It is analysed and refined
It is then tested and modelled
Then evaluated against the brief – many versions fail but that then informs development to make the idea better
The cycle then repeats and if the product is successful it is then made and sold on the market
User-Centred Design
This is when designs are based on fulfilling the needs and wants of the Users/ Clients at every stage of the design process
Questioning and testing is ongoing and is often found through interviews, questionnaires, surveys, etc
Numerous companies work in teams, and has been shown to improve the range and quality of ideas produced
Collaborative Approach
Working with others to share data and solving problems and coming up with design proposals can help with creativity
Planning the layout for the correct sequences e.g. inputs, outputs, timings, etc
Electronics and mechanical systems need an ordered and logical approach
Often uses diagrams to show systems in a visual way
Systems Approach
Usually used for electronic products
Iterative Design | 
Advantages | Disadvantages
Consistent testing helps solve problems earlier Constant feedback Easy evidence of progress | Designers can loose sight of “the big picture” Time consuming
User-Centred | 
Advantages | Disadvantages
User feels listened to Makes sure the product meets their needs | Requires extra time to get customer feedback If focused on just one person it can limit appeal to others
Systems Approach | 
Advantages | Disadvantages
Does not need specialist knowledge Easy to communicate stages Easy to find errors | Sometimes over-simplifies stages Can lead to unnecessary stages
Collaborative Approach | 
Advantages | Disadvantages
Gets multiple opinions and a range of views Working in groups can produce more ideas | Can be difficult to design ideas with opposing views Can be difficult to find time to communicate with multiple people

## Slide 4
Environment
The 6Rs | Meaning
Reuse | To use a product again either for the same purpose or a different one
Reduce | To have less of material/packaging/pollution when making products by making them more efficient
Recycle | Breaking down and forming the material into another product
Refuse | Customers not buying or supporting products that make an environmental impact
Rethink | Designers and customer rethinking their decisions when making and buying products.
Repair | Fixing a product rather than throwing it away. Extending its life rather than using more resources to make another Often products are Designed for Maintenance so can easily be repaired. E.g. Using screws so even non-specialists can take a product apart, or using components that can easily be replaced like fuses or batteries
Sustainability is maintaining our planet and its resources and making a minimal negative impact | 
Finite Resources Will run out of eventually | Infinite Resources Can be re-grown and re-bread. Will not run out of
Plastics | Paper
Metals | Boards
Polymers (Textiles) | Natural Timbers
 | Cotton
 | Leather
What can we do to reduce environmental impact or products and manufacture?
Life Cycle Assessment
This is when a designer looks at the environmental impact a product makes over its life time and how it could be reduced. Including:
Impact of materials
Impact of processes
Product Miles (how far a product has to travel to get from factory to consumer)
Impact while in use
Impact when disposed of (6Rs)
Repairing products rather than throwing them away
Recycling products and materials
Reducing Product Miles buy making the product in the country it is sold in
Reducing Pollution by using less plastics, efficient manufacture, less waste and using renewable energy (like solar and wind)
Using less finite resources
Planting more trees to reduce deforestation
Planned Obsolescence | This is where products “die” after a certain amount of time. E.g. Disposable cups, Phones, Lightbulbs, Printer Ink, etc This can have a big environmental impact as customers are throwing away lots of products, and resources are being used to create new ones.

## Slide 5
Modern and Smart Materials
Modern Materials are materials that have been developed recently |  | 
Material | Key info | Examples
Corn-starch Polymers | These are plant-based polymers that are a replacement for plastics that are biodegradable but cannot be recycled. | Plastic bottles, tubs, food containers, etc
Flexible MDF | Made in the same way as normal MDF but with grooves cut into the surface so it is flexible. Flexiply is the same but for Plywood. These can easily be shaped into curves | Modern furniture, interior walls and room dividers
Titanium | High strength to weight ratio. Doesn’t corrode or rust. Suitable for medical use as its hypo-allergneic | Prosthetics, medical applications, sports cars, etc
Kevlar | A woven polymer with a high strength to weight ratio. | Bullet-proof vests, tyres, helmets, etc
Smart Materials are materials that change and react to the stimuli |  | 
Material | Key info | Examples
Thermochromic Pigments | Change colour in reaction to heat | Kettles, baby bottles, etc
Photochromic Pigments | Change colour in reaction to light | Colour changing glasses, windows, etc
Shape Memory Alloy | Returns to its original shape, in reaction to heat | Braces and glasses
Polymorph | Granules that once exposed to hot water, become a modelling material (like a dough or clay) | Modelling and repairs
Papers and Boards
Papers and Boards come from trees. The Stock forms for papers are: rolls, sheets, A4, A3, etc |  | 
Material | Key info | Uses/ Examples
Cartridge Paper | Thick white paper, completely opaque and more expensive than photocopy paper | Sketching, ink drawings
Layout Paper | Light, semi-translucent, good for blending inks and artist markers | Sketching, drawing and some tracing
Corrugated Cardboard | Strong but light. Rigid triangles of card sandwiched between a top and bottom layer. | Outer packaging, food packaging
Duplex Board | Light card with white outside layers. Waxy coating can be added | Cheap packaging. If waxy coating is applied, can be used for food
Foil-lined Board | White card coated with a thin aluminium layer. Foil is great for insulation and water resistance | Takeaway containers
Solid White Board | High-quality white card with a smooth finish. Stiff and holds colours well | Greetings cards, packaging and advertising
Paper is made by first making pulp. Pulp is a mix of tree fibres and water. This is cooked and bleached white, and adding any other additives.
The pulp is then drained and goes through Calendering where the pulp is drained and goes through rollers to convert it to its stock forms
Primary Processing of Papers and Boards

## Slide 6
Hardwoods come from Deciduous Trees. These trees loose leaves in winter and grow fruit and flowers in spring |  | 
Material | Key info | Examples
Ash | Flexible, tough and shock resistant | Sports equipment Tool Handles
Beech | Fine finish, tough and durable | Toys, furniture and veneers
Mahogany | Easily worked, durable, high quality finish | High-end furniture
Balsa | Very soft and spongy. Light | Modelling
Oak | Tough, durable and hard | Flooring, furniture and veneers
Softwoods come from Coniferous Trees. These have thin, needle-like leaves and grow all year round. Often have pine cones and sometimes nuts and seeds |  | 
Material | Key info | Examples
Larch | Durable, tough, good water resistance and finishes well | Furniture, flooring and used outdoors
Pine | Light, easy to work with but can split | Cheap furniture, construction and decking
Spruce | Easy to work with, high stiffness but can decay quickly | Furniture, musical instruments and construction
Softwoods are generally cheaper than hardwoods as they are more available, since they grow quicker.
But because man-made boards are manufactured they are cheaper than timbers. Man-made boards also come in a better variety of sizes since they don’t depend on tree growth.
Stock forms for both include; sheets, dowel, planks, etc
Manufactured boards are made from wood chips/dust/ layers and glue. |  | 
Material | Key info | Examples
Chipboard | Prone to chipping but good compressive strength. Not-water resistant | Flooring, low-end furniture, flat-pack
MDF | Rigid and stable. Easy to finish. Absorbs liquid easily | Flat-pack furniture and kitchen unites
Plywood | Very stable. Exterior veneer can be used from more expensive woods | Shelving, furniture, toys
Trees are cut then converted into planks by cut using saws
It is then seasoned to reduce the moisture in the wood. This is done by either:
Air-drying – Planks are stacked and air allowed to circulate; causing evaporation
Kiln-drying – Where planks are put into a kiln and dried rapidly. This process is more costly than air-drying
Manufactured boards can be either be made by lamination or compression
Lamination – Layers of woods and adhesive are layered and compressed together. Usually with a more expensive wooden veneer on the top
Compression – Wood is shredded, heated and compressed with adhesive under extreme pressure
Woods and Boards
Natural Timbers
Man-Made Boards
Primary Processing of Papers and Boards

## Slide 7
Ferrous Metals contain iron and are magnetic and rust |  | 
Material | Key info | Examples
Low Carbon Steel | Tough and ductile and easily machined and welded | Construction, screws, cars
High Carbon Steel | Hard and wears well | Tools, blades and knives
Cast Iron | Hard but brittle. Easily cast but hard to machine | Pots, pans, vices
Non-Ferrous Metals do not contain iron, aren’t magnetic and don’t rust |  | 
Material | Key info | Examples
Aluminium | Light, high strength to weight ratio and ductile | Pots, pans, cars, cans
Copper | Ductile, malleable and good conductor | Plumbing supplies and cables
Tin | Soft, malleable and good conductor | Used as a protective coating
Metals come from ores in the ground. Stock forms are sheets, bars and rods
Alloys are mixtures of 2 or more metals to get the best of their properties |  | 
Material | Key info | Examples
Brass | Malleable and easy to cast | Musical instruments, plumbing
Stainless Steel | Doesn’t rust, hard and smooth | Cutlery, medical tools, etc
Metals are mined from the earth and then go through an extraction process
Extraction happens by putting the ore in a blast furnace
The metal is then separated from the waste material
Metals, Alloys and Plastics
Metals
Alloys
Primary Processing of Metals and Alloys
Plastics come from crude oil. Stock forms are sheets, powders, granules and rods
Plastics
Thermoplastics can be reheated and reshaped and infinite amount of times |  | 
Material | Key info | Examples
PET | Easily blow moulded, food safe and easily recycled | Bottles, packaging, etc
PVC | Flexible, tough, easily extruded | Pipes, tape, hard hats
HIPS | Flexible, lightweight, food safe and easily vacuum formed | Containers and yoghurt pots
Acrylic | Tough, brittle, easily scratched | Car lights, baths, displays/ signs
Thermosets once heated and set cannot be reshaped |  | 
Material | Key info | Examples
Melamine Formaldehyde | Food safe, hygienic, hard and brittle | Kitchenware and work surfaces
Urea Formalehyde | Good insulator, hard and brittle | Electrical casings, buttons and handles
Polyester Resin | Strong, heat resistant, can be transparent | Coatings, casings
Primary Processing of Plastics
Crude oil is extracted from the earth and then processes into different types of fuels, etc. This is called Fractional Distillation
A process called Cracking then converts the large hydrocarbon molecules into plastics

## Slide 8
Name of Process | Diagram | Material | Products Made | Key info
Screen-printing |  | Papers and Textiles | Posters, signs and t-shirts | Screen printing places paint on top of a screen. The screen has a stencil embedded in it, so when the paint is passed across it the desired shape is printed underneath. Good process in one-off and batch production as often done by hand
Offset Lithography |  | Papers and card (thin, flexible plastics) | Posters, newspapers, plastics bags | Rollers containing the colours and water go onto the plate cylinder. The water stops the colours sticking to certain places, creating the shape. The shape is transferred between rollers and onto the material. Can be used at batch and mass production
Lathe Turning |  | Wood and metal | Chair legs, baseball bats )(cylindrical items) | Material is placed between the tail stock and the headstock and spun at high speed. The material is then cut using specialist tools (either by hand or my automated machinery) to the desired shape. Can be used in one-off and batch production
Die Casting |  | Metal | Car parts, engine components, etc | Molten metal is poured into a chamber and a plunger forces the metal through the nozzle into the mould. Unlike sand casting, the mould is reusable. Good process for both one-of and batch production
Injection Moulding |  | Plastics | Chairs, toys, etc | Plastic granules are poured into the hopper and onto the screw. The screw moves the material towards the heater where it turns into a liquid. The liquid is then forced into the mould, cooled and released. Great process for mass production as it makes 100s+ of products at once, to a identical standard.
Blow Moulding |  | Plastics | Plastic bottles | A Plastic parison is heated and put into the mould. The parison is then filled with air (like blowing up a balloon) and is forced to fit the mould shape. It is then cooled and then released. This is a great process for mass producing bottles.
Production Processes

## Slide 9
Production Techniques and Systems
CAD Computer Aided Design | 
Examples; 2D Design, Autodesk Inventor, Fusion 360, Photoshop, etc | 
Advantages | Disadvantages
Easy to change designs Designs are easily saved and sent Can be worked on by multiple people simultaneously Can be used for virtual testing Can produce high-quality designs | Complex and time-consuming to learn Expensive to buy PCs can crash or be hacked – causing work to be lost Takes up PC memory
CAM Computer Aided Manufacture | 
Examples; 3D Printing, Laser Cutting, CNC Router, Automated Machines and Robotics, etc | 
Advantages | Disadvantages
Faster and more accurate than traditional tools Repetitive accuracy/ consistent outcomes Machines can run 24/7 | Expensive to buy the equipment, etc Training takes cost and time Need specialists to maintain and repair the machines Dependence on CAM can cause unemployment
Flexible Manufacturing Systems
This is where automated machines are adaptable and can produce different products if needed. If a manufacture is making a product with machines that are just dedicated to specific tasks they have to be reprogrammed and re-tooled before changing to a new task. This is time consuming and expensive. Examples include; CNC Machines, 3D Printers, Laser Cutters, Robotic arms, etc
Just-in-Time (JIT) Manufacture | 
This is where manufacturers only order materials, parts, etc when needed. The customer’s order triggers the production process and the resources needed for that order are the only ones bought. This can be used in any scale of production but is particularly useful for one-off production. | 
Advantages | Disadvantages
Saves on warehouse and storage costs Money is not tied-up in stock Little/minimal waste Customer often pays in advance so money is secure before production | All production stops if a part/ material is missing Needs to have a fast, reliable and good quality supply chain to work properly Can be time-consuming
Lean Manufacturing
This is where waste and energy is kept to a minimum. This helps manufacturers save money and resources in production, as well as helping minimise the environmental impact of producing products.

## Slide 10
Scales of Production
Name/ Type | How many it makes | Key Info | Examples of Products
One-off Production | 1 | Also known as Bespoke or Prototype manufacture Custom-made products Specialist workers/ skills Specialist machines and materials High Quality but expensive | Towers / Bridges One-off Houses Custom made clothes
Batch | 10s-1000s | Uses a mix of workers and machinery Uses jigs, moulds and templates to help make identical products Stations of workers e.g. cutting station, painting station, etc Can have some variation e.g. colour, finish, flavour | Baked foods Limited edition car Socks Chairs
Mass | 10,000s - 100,000s | Big assembly lines (and sub-assembly lines) Heavily automated Standard and identical products Little worker input | Cars Bottles Microchips Plain shirts
Continuous | 100,00s + | 24/7 production Heavily automated Standard and identical products Little worker input | Energy Water Paper Plastic
One-off Production | 
Advantages | Disadvantages
Custom made High Quality Materials High Quality Craftsmanship | Time consuming Specialist training for workers Expensive to buy
Batch Production | 
Advantages | Disadvantages
Lower cost than one-off Jigs, moulds and templates help products look identical Can have some variety | High storage costs Jugs, moulds and templates have to be checked Workers can become bored on their station
Mass Production | 
Advantages | Disadvantages
Large amounts made at once All products are identical and to same standard Using automation reduced human error | Initial starting costs are high If production line stops, the product can’t be made Workers become bored monitoring machines and repetitive tasks
Continuous Production | 
Advantages | Disadvantages
Large amounts made at once All products are identical and to same standard Using automation reduced human error | Initial starting costs are high If production line stops, the product can’t be made Workers become bored monitoring machines and repetitive tasks

## Slide 11
Work of others and Customer Research
Image/ Example | Designer | Design Movement | Key info
 | William Morris | Arts and Crafts | British designer in 1880s Simple natural crafts Useful and beautiful products (wallpapers, cushions, etc)
 | Charles Rennie Mackintosh | Art Nouveau | Scottish designer in 1860s – 1920s Known for light and shadow Created stained glass and furniture Inspired by nature and geometric lines
 | Ettore Stottas | Memphis | Italian designer in the 1950s/60s Enjoyed making everyday objects wacky and bold Used lots of bold colours and black lines
Image/ Example | Brand | Key info
 | Alessi | Italian Design Company Homeware and kitchen utensils “Post-modern” style Phillipe Starke is a major designer
 | Apple | USA-based tech company Famous for iconic designs of iPod and iPhone Steve Jobs and Johnathon Ive are major designers Known for innovative and modern design
 | Dyson | British engineering company Famous for vacuum cleaners and innovative technology James Dyson is a major designer
Research
Work or Others
What methods of research can be used to find information?
Case studies
Questionnaires and surveys
Product Analysis
Materials testing
Social media and email
Interviews
Research can be divided into 2 categories; Primary Research and Secondary Research.
Primary is research you complete yourself.
Secondary is research from resources others can gathered e.g. books, magazines and internet
Primary research is generally more reliable as it is done by the person using it and can double-check the data
Another key piece of research, is Anthropometrics and Ergonomics. This helps develop the sizes of products, etc to make sure it fits the User | 
Anthropometrics | The study of measurements of the human body. E.g. Knowing the grip width of a palm, if designing a new travel coffee cup
Ergonomics | The application of anthropometrics to ensure products are safe and comfortable to use. This can also include; size, material, appearance, brightness, sound and texture. E.g. making sure the travel cup is the correct size, and an insulating smooth material to make it comfortable to hold for long periods